## Slide 1: GLIM Map Building Automation System
Abdullah AlMusalami
Senior Robotics Engineer
May 2026

## Slide 2: System Overview

## Slide 3: GLIM Map Building Automation System
3-Phase System Architecture

## Slide 4: Phase 1 · Docker Environment

## Slide 5: Phase 1 · Docker Environment
Environment Setup
Base image: nvidia/cuda:13.2 + Ubuntu 22.04
ROS2 Jazzy Desktop
GLIM — GPU-accelerated 3D SLAM (koide3 PPA)
All dependencies pre-installed: GTSAM 4.3, Iridescence, GLFW, METIS
GTSAM version conflict resolved inside the container — zero manual steps
ROS2 bag files mounted at runtime ( -v /path/to/bags:/bags )
GPU passthrough: --gpus all (requires nvidia-container-toolkit)

## Slide 6: Phase 2 · Interactive CLI Wizard

## Slide 7: Phase 2 · Interactive CLI Wizard
Full Pipeline: ros2 run slam_glim main

## Slide 8: Phase 2 · CLI Wizard
Step 1: Bag Preparation + Step 1.5: Sensor Configuration
Step 1 — Bag Preparation:
  User provides the bag file path
  ROS1 .bag? → auto-convert to ROS2 .db3 (rosbags-convert)
Step 1.5 — Sensor Configuration:
  User edits ONE YAML file: config/user_config.yaml
  Only 3 fields required:
    imu_topic: /imu/gravity
    lidar_topic: /velodyne_points
    T_lidar_imu: [tx, ty, tz, qx, qy, qz, qw]
  System auto-fills all 6 GLIM JSON config files — user never edits JSON

## Slide 9: Phase 2 · CLI Wizard
Step 2: Sensor Validation
Runs GLIM's built-in validator_node against the bag
  Checks: IMU rate, LiDAR rate, topic existence, gravity vector detection
Prints a human-readable report to the terminal
Human reviews the report → fix config/user_config.yaml if needed
Catches misconfigured topics before wasting a full SLAM run
Press Enter when satisfied to proceed to SLAM

## Slide 10: Phase 2 · CLI Wizard
Steps 3–4: GLIM SLAM Execution
Pipeline selection (asked every run):
  [1] GPU — VGICP_GPU + CUDA (default, RMC robot)
  [2] CPU — VGICP CPU, no GPU required
  [3] LiDAR-only — CT-ICP, no IMU required
Config review: shows IMU topic, LiDAR topic, T_lidar_imu — confirm before SLAM starts
Mode selection:
  [1] Live Viewer — glim_rosnode + ros2 bag play + Iridescence 3D viewer
  [2] Fast Offline — glim_rosbag, no viewer, faster than real-time
Dump auto-saved → maps/<bag_name>_<YYYYMMDD_HHMMSS>/

## Slide 11: Phase 2 · CLI Wizard
Steps 5–6: Map Refinement & Merging
Step 5 — Edit / Modify Map:
  Opens GLIM map_editor GUI with the current dump
  Add or remove loop closures, re-optimize the pose graph
  Loop: edit more? → repeat until satisfied
Step 6 — Merge Maps:
  User provides a second dump directory
  map_editor loads both dumps → user aligns and merges in the GUI
  Merged dump path saved for the export step

## Slide 12: Phase 2 · CLI Wizard
Steps 7–8: Map Export & 2D Map Generation
Step 7 — Export Map (fully automated, no GUI):
  Reads dump binary: points_compact.bin (float32 XYZ) + data.txt (T_world_origin)
  Transforms all submaps to world frame → voxel filter 0.05 m
  Writes ASCII PCD v0.7 → maps/<run>/map.pcd
  No PLY step — dump binary is parsed directly in Python
Step 8 — 2D Occupancy Map:
  Ground detection: z-histogram from 1st percentile, find floor peak
  Height filter: floor+0.3 m to floor+3.0 m
  Output: map_2d.pgm + map_2d.yaml (nav2_map_server compatible)

## Slide 13: Phase 2 · CLI Wizard
Step 9: POI Registration
RViz2 opens automatically with the 3D PCD map displayed
Select the Publish Point tool in the RViz2 toolbar (crosshair icon)
Click any point on the 3D cloud
Red sphere + text label appear at the clicked location
POI saved automatically to YAML in maps/<run>/POI_Poses/
YAML format:
  pois: [ { id, name, timestamp, frame_id, position, orientation } ]
  orientation: identity quaternion — compatible with ROS2 nav goals

## Slide 14: Phase 3 · Web Dashboard

## Slide 15: Phase 3 · Web Dashboard
Browser-Based Interface (Coming Soon)
Replaces CLI wizard with a web page — same pipeline, zero terminal interaction
3D map viewer in the browser (Three.js / Potree)
POI editor: click-to-place on the 3D map in the browser
Live robot tracking: WebSocket stream of robot pose overlaid on the global map
Map library: browse all saved map runs with metadata and thumbnails
OEM export: download PCD + 2D map + POI YAML for distribution
Architecture:
  Flask / FastAPI backend → calls the same step modules as the CLI
  Design constraint: all step modules accept decisions as parameters (no input())

## Slide 16: Implementation Plan
Phase 2 — Implementation Order
1. export_map.py — Binary dump → PCD (core unique logic, first)
2. convert_map.py — PCD → 2D occupancy grid
3. pcd_publisher.py + poi_selector.py (copy + adapt from glim_test)
4. view_map.launch.py + view_map.rviz
5. config_setup.py — user_config.yaml → GLIM JSON files
6. slam_runner.py — GLIM launch: pipeline select + two modes
7. validator.py — Sensor validation subprocess + report
8. bag_convert.py — ROS1 bag conversion wrapper
9. map_editor_launcher.py — Map editing / merging subprocess
10. main.py — CLI wizard orchestrator (wires all steps)